## Slide 1
Codec – Encoding Camera
Pairing Mechanism

## Slide 2
Steps for setup of new room system:
Unbox Codec and Encoding Camera(s)
Install codec and wait for network settings to be detected by the Codec
Proceed to other setup in codec like CUCM settings, etc.
Power on the Encoding cameras and let them connect to the
WI-FI/Bluetooth (Wi-Fi Direct)
Codec/Proximity app searches for unpaired Encoding Cameras in the network
Which are in configuration mode
Select the desired encoding camera(s) for pairing based on the LED blinking on the camera.

## Slide 3: Technologies
Pairing can be performed with either Bluetooth or Wi-Fi direct technologies.
We list down the benefits and disadvantages of each of these .
We initially approached using an IP only approach, but faced some bottlenecks.

## Slide 4: Challenges with IP Multicast
Can it work over NAT/VLANs?
What are the assumed router configurations for Multicast to work 100% of time?
Multicast over Production networks?
Multicast was not successful when tested with In house Networks in CETG, Bangalore.
Multicast didn’t work over a Local NAT?
Router Configurations For multicast will make the out of box very frustrating for the customer.

## Slide 5: Sample working (Proximity)
Proximity App
Smartphone looks for devices.
-> Encoding Cameras in config mode always connect
-> All codecs connect
Camera 27346
Camera 27376
Camera 27856
Room #1
Room #2

## Slide 6: Working With Proximity
Proximity App
Static IP Address
Blink LED
Camera 27346
Camera 27346
Alias
Wi-Fi SSID
Wi-Fi Password

## Slide 7: Working With Proximity
Proximity App
Camera 27346
Camera 27376
Camera 27856
Room #1
Room #2
Room #1
Room #2
Camera 27346
Camera 27376
Camera 27856

## Slide 8
Admin’s Perspective
Pair with Encoding Camera
Lookup MAC ID
Scan Network

## Slide 9
Admin’s Perspective
SCANNED DEVICES
Search
PAIR
Blink LED
PAIR
PAIR
PAIR
Blink LED
Blink LED
Blink LED
Camera 00A6HJH
Camera 00A6JJH
Camera 00A9HJH
Camera 0076FJH

## Slide 10
Admin’s Perspective
SCANNED DEVICES
Search
PAIR
Blink LED
PAIR
PAIR
PAIR
Blink LED
Blink LED
Blink LED
Camera 00A6HJH
Camera 00A6JJH
Camera 00A9HJH
Camera 0076FJH

## Slide 11
User’s Perspective
PAIRED DEVICES
Search
Use in Call
Use in Call
Use in Call
Use in Call
Paired Camera Alias 1
Paired Camera Alias 2
Paired Camera Alias 3
Paired Camera Alias 4

## Slide 12: Bluetooth
Connections between Bluetooth enabled electronic devices allow these devices to communicate wirelessly through short-range, ad hoc networks known as piconets
Piconets are established dynamically and automatically as Bluetooth enabled devices enter and leave radio proximity
Operates in 2.4Ghz band
3 Power classes
Frequency Hopping Spread Spectrum

## Slide 13: Bluetooth 4.2
Enables IoT with support for IPv6,WPAN or Bluetooth Smart gateways
Bluetooth smart is smarter in terms of Privacy, Power efficiency and Security
Bluetooth Smart even faster with throughput speed and increased packet capacity

## Slide 14: Wi-Fi direct
Protected by WPA2, Wi-Fi Protected Setup.
Immediate utility: Can use any smart phone irrespective of previous pairing history.
Simple API for development. least hardware dependency.
Avoids additional configuration complexity and potentially exposure of network resources.
Wi-Fi Peer-to-Peer technology has been designed to be implemented on the same silicon as the majority of new devices that support Wi-Fi. As a result, the new capabilities will not require a significant increase in software or CPU capability.
Support for legacy Wi-Fi devices, as clients only.
Power management to reduce power consumption.
Persistent groups capability.
Support for concurrent connections. Especially beneficial for Wi-Fi drishti case.

## Slide 15: Bluetooth vs Wi-Fi Direct
 | Bluetooth | Wi-Fi Direct
Speed | 25 Mbps | 250 Mbps
Security | 128 bit AES | WPA2 256 bit AES
Distance | 1m – 100m | 200 m
Power | Less with Low Energy (2.5mW) | Relatively more (30 -40 % less with WMM Power Save)
Backward Compatibility | N | Y
No of Devices | 7 active slaves (upto 248 devices but they should be in sleep mode) | 1 to Many
Pairing | Device discovery protocols like SDP | Challenging as it lacks discovery protocols
IOT | Bluetooth 4.2 | Obvious choice [ubiquity in homes and devices]

## Slide 16: Functionalities in EncCam
LED to indicate these states
blink on request from CODEC
Green to show configured state
Red to show Unconfigured state
Physical switch to RESET or UNPAIR in the event of codec going down without unpairing.
Both Codec/camera will send health pings every few seconds and retry n number of times in cases the pings are not successful.
After N retries , the camera is presumed to have gone down and is unpaired

## Slide 17: Use cases
When Codec goes down/ New codec
When the codec goes down its safe to unpair the cameras with the codec and move the Camera to Config mode. (This will be discovered based on periodic health pings between Camera/codec)
When the Encoding camera goes down(Reboots)
When an Encoding camera Reboots , there is already an established communication channel established between Codec/camera. The codec can reinitiate the connection.
(If reconnection doesn’t happen in a given interval of time, we can move the camera to Config stage again)
Reset of Encoding camera.
In any unwanted event, We can always access the physical reset button on the camera to move it into Config mode again.

## Slide 18
Admin’s Perspective
Sudden Encoding Camera Outage
MAC ID

## Slide 19
Admin’s Perspective
Sudden Codec Outage

## Slide 20
Admin’s Perspective
Codec retrieves IP address, subnet mask, etc. as well call control settings.
Encoding Camera gets IP Address.
Encoding camera is now into Configuration mode.
Encoding camera waits for reply request message from anticipating codec.
Codec sends a reply request message to the multicast address whose members are all encoding cameras.
Encoding camera(s) receive the reply request on multicast address + Port combination.
Encoding cameras reply on unicast to the codec with IP address details along with video feed/ JPEG image
Codec receives the reply(s) from the encoding camera(s) and lists down the encoding cameras in the UI for admin to select to pair
Once the encoding camera(s) are selected, the security keys are exchanged between the camera(s) and codec to establish a secure communication channel.
The encoding camera(s) are now out of the configuration mode. They are not discoverable by any other codec hereon.

## Slide 21
Admin’s Perspective
Steps for setup of new room system:
Unbox Codec and Encoding Camera(s)
Install codec and wait for network settings to be detected by the Codec
Proceed to other setup in codec like CUCM settings, etc.
Place encoding camera(s) and plug ethernet cable.
Codec searches for unpaired Encoding Cameras in the network which are in configuration mode
Select the desired encoding camera(s) for pairing based on the selfview + LED blinking on the camera.
Once the encoding camera(s) are selected, the security keys are exchanged between the camera(s) and codec to establish a secure communication channel.
The encoding camera(s) are now out of the configuration mode. They are not discoverable by any other codec hereon.

## Slide 22
User’s Perspective
In the context of Encoding camera pairing, the User does not get pairing privileges. The user is able to configure the call by choosing amongst the Encoding cameras that are already paired with that specific codec. To aid the User to decide on the Encoding cameras, guiding self-view will be provided in the UI.
Steps followed by the User:
Chose the codec to be used for the desired call
In the codec, chose amongst the paired Encoding cameras to be used for the call.
Once the Encoding cameras are selected, the call can be started.
There will be a self-view displayed corresponding to each of the cameras, along with a blinking LED suited for identification purpose. This will aid the User to select the correct Encoding cameras for the call.
If no cameras are explicitly selected, a default camera will be assumed for the call.