## Slide 1: Video Over Wifi
Kavitha

## Slide 2: Agenda
Use cases
Problems
Statistics
Improve Signal Strength

## Slide 3: Use Case
Flexibility of not having to deal with wires is a compelling reason to use 802.11 for video streaming

## Slide 4: Use case
Encoding Camera 1
Encoding Camera 2
Encoding
Camera 3

## Slide 5: Speeds

## Slide 6: Measurements
g speed
Place Link Quality Signal Level Total Speed Near WAP 70/70 -26 dBm 21400 kbps Kavitha's 66/70 -44 dBm 20700 kbps Sofa near Gijo 55/70 -55 dBm 16400 kbps Sofa near Resmi 52/70 -58 dBm 18000 kbps Near Entrance Door 36/70 -74 dBm 4180 kbps Reception 23/70 -87 dBm 30 kbps (disconnected) Near Panna 34/70 -76 dBm 5100 kbps n speed Place Link Quality Signal Level Total Speed Near WAP 70/70 -23 dBm 52453 kbps Kavitha's 66/70 -43 dBm 45900 kbps Sofa near Gijo 57/70 -53 dBm 39000 kbps Sofa near Resmi 49 /70 61 dBm 32000 kbps Near Entrance Door 34/70 -76 dBm 7500 kbps Reception 26/70 -84 dBm 24 kbps (disconnected) Near Panna 43/70 -67 dBm 23017 kbps

## Slide 7: Wifi analyzer

## Slide 10: Wifi analyzer

## Slide 11: wavemon

## Slide 12: wavemon

## Slide 13: wavemon

## Slide 16
Ping –f –Q hex <IP address>
TOS ms 0 133.570 8 150.624 48 1528.071 160 439.801 224 11.752

## Slide 17: Packet Loss

## Slide 18: Limitations in current 802.11 mechanisms
Limited prioritization
Lack of inter-layer communication
Limited set of QoS parameters
Limited capability to dynamically tweak QoS parameters
Lack of content-specific methods

## Slide 19
  Interference, path loss
  Limited number of channels in unlicensed bands
  Channel characteristics constantly change (dynamic)
Medium access non-deterministic (802.11 is originally designed for data)
STA physically moves in the same BSS
Inter-stream synchronization
  Between audio rendered at remote speakers and video
  Between one video stream and multiple audio streams

## Slide 20
Keep firmware updated[router/adaptor]
Wifi range Extenders and repeaters
Distance impedes performance
Signal bounce around beamforming
Interference
Router position
Antennas
less than 1% packet loss as "good" for streaming audio or video, and 1-2.5% as "acceptable"

## Slide 21: WMM
Wi-Fi Multimedia (WMM), previously known as Wireless Multimedia Extensions (WME), is a subset of the 802.11e wireless LAN (WLAN) specification that enhances quality of service (QoS) on a network by prioritizing data packets according to four categories. Network administrators can change priority levels as they see fit.
Ranging from highest priority to lowest, these categories are:
Voice: Giving voice packets the highest priority enables concurrent Voice over IP (VoIP) calls with minimal latency and the highest quality possible.
Video: By placing video packets in the second tier, WMM prioritizes it over all other data traffic and enables support for three to four standard definition TV (SDTV) streams or one high definition TV (HDTV) stream on a WLAN.
Best effort: Best effort data packets consist of those originating from legacy devices or from applications or devices that lack QoS standards.
Background: Background priority encompasses file downloads, print jobs and other traffic that does not suffer from increased latency.